Title
Telecommunications
Pincher Creek SAR

---
Product
Why?
Why is communications important in SAR?
Why professionalism?
Why standards?

---
Why?
The biggest problem you will ever experience in a SAR situation is lack of communication.
Critiques: "The first problem is always communications"
communicating clearly with other groups
expectations of other groups (RCMP)
working efficiently

---
Methods of Communication
What communications methods have you seen used in SAR?

---
Radio Theory
all the wireless electronic communications methods are using radio waves
radio waves are electromagnetic radiation, same as light, longer wavelength

---
Radio Theory
Wavelength / Frequency
All radio transmissions have a wavelength
The speed of radio is the same: 3 x 108 m/s (speed of light)
The number of waves received at a spot per second changes with the wavelength. Shorter wavelength, higher frequency.
Bands:
VHF: 30 - 300 MHz: 10 m to 1 m
UHF: 300MHz - 3 GHz: 1 m to 10 cm

---
Radio Theory
Longer wavelengths bend around hills easier
Shorter frequencies can carry more information, packed closer together
Some frequencies bounce off the high atmosphere easier

---
Radio Theory
Simplex: Transmit and receive on same frequency
one at a time
Duplex: Transmit and receive on different frequencies
simultaneously
typically using tower: repeater channels, cell phones

---
Radio Theory
Power
Power is measured in Watts (W)
The more power the further the signal can be received
Generally: double the distance, 4 times the power
advantages to less power?
Typical: 0.5 W FRS, 2 W GMRS, 3 W commercial handheld, 30 W commercial mobile, base station

---
Radio Theory
Polarity
different types of antennas transmit and receive with different polar orientations
keep antennas upright

---
Radio Theory
Signal Encoding
AM: Amplitude Modulation
FM: Frequency Modulation
more resistant to static interference
Generally: established by band, fixed in radio

---
Radio Theory
Squelch
radio waves always present
Electromagnetic noise, interference
suppress speaker based on signal strength
squelch button
CTSS: Continuous Tone Squelch System
very low frequency tone added to transmission, if not present, suppress speaker
FRS sub-channels

---
Radio Theory
“Channel”
Combination of Frequency, Polarity, Encoding, and Squelch to transmit and receive on

---
Radio Anatomy
power source
microphone
transceiver / modulator
antenna
demodulator / receiver
squelch / speaker

---
Types of Radios
Hand held

---
Types of Radios
Mobile

---
Types of Radios
Base Station

---
Types of Radios
Repeater

---
Connectors
PL259 or UHF connector

---
Connectors
BNC connector

---
Connectors
UHF to BNC

---
Connectors
SMA Connector

---
Connectors
F to TV

---
Use of Radios
Handhelds
Battery Replacement
Using the controls
Posture of the user

---
Use of Radios
Mobile Radio setup and use
Base Radio setup and use

---
Use of Radios
Equipment and channels we have access to
Channel 1 – Emergency Services repeater
Channel 2 – Emergency Services talk-around (Simplex)
Channel 9 - Tac 9 (RCMP) – Simplex

---
Protocols
Communication Protocols
set by laws of physics
set by international treaties
set by Canadian law
set by SARA standard
set by professional expectations
Physics: Do not cut into a message being sent. Listen before you send.

---
Protocols
Professional expectations:
Sound professional. Absolutely everyone is listening.
Make sure your information is clear, concise and short. Think before you speak, not during.
Speak slow and clear.
Use simple words.

---
Protocols
Standard Words and Phrases
used internationally
pronunciations are tuned to world-wide speakers
vocabulary comes from both English and French
ITU Alphabet

---
Protocols
Numberss
3-Tree
4-Fower
5-Fife
9-Niner
Hundred
TOUsand
Decimal

---
Protocols
Calling procedures
Treat like all your job is, is to pass on written messages. Think telegraph.
Call Signs
Format: (Dest Call Sign), THIS IS (Source Call Sign), (message) OVER (or OUT)

---
Protocols
This Is ...
Over - I have finished talking and I am listening for your reply. Short for "Over to you."
Out or Clear - I have finished talking to you and do not expect a reply. Channel available for other use.
Roger - Information received.
Copy - I understand what you just said (after receiving information).
Acknowledge - confirm you've received

---
Protocols
Stand By
Go Ahead
Correction / I Say Again / Say Again
Read Back / Message is / That Is Correct
Words Twice

---
Protocols
Shortening the format
(Dest Call Sign)x3, THIS IS (Source Call Sign)x3, (message) OVER (or OUT)

---
Call Signs
All Stations
Net Control, “Control”

---
Call Signs
SARA Standard:
A - Prefix assigned to Medical Teams
B - Prefix assigned to specialized resources, not just boats - boats, ATVs, Bikes, Horses
D - Prefix assigned to Dog Teams
H - Prefix assigned to Helicopter units or the aircrafts call sign may be used e.g.. C-GAHM
S - Prefix assigned to Search teams
T - Prefix assigned to Tracking teams

---
Protocols
Specialized messages: answers
Affirmative / Negative
Wilco - Will Comply (after receiving directive/request).

---
Protocols
Specialized messages: time
Use the 24 hr clock to tell time.
Hundred
Zulu – UTC (GMT) aviation

---
Protocols
Specialized messages: radio check
How Do You Read?
Strength / Clarity
1 - (unreadable)
2 - (breaking up)
3 - (readable with difficulty)
4 - (readable)
5 - (perfectly readable)
5 x 5, “loud and clear”

---
Protocols
Specialized messages: emergencies
MAYDAY / PAN PAN / SECURITY

---
Protocols
General messages
use of plain language
not “10 code”: 10-4
exceptions:
SARA standard: Code: 1062 means turn radio off or move away from group.
Death or injury relayed in code or special word by mgmt., instructions.
Pincher SAR's 5 codes

---
Example
contact, basic message
TEAM ALPHA, THIS IS BASE, OVER
BASE, THIS IS TEAM ALPHA, GO AHEAD, OVER
TEAM ALPHA, ... OVER
BASE, ROGER OUT
PROCEED TO UTM 915026 AND SWEEP TRAIL TO BOULTON CREEK

---
Example
BASE, THIS TEAM BRAVO, HOW DO YOU READ?, OVER
TEAM BRAVO, THIS IS BASE, READING YOUR STRENGTH 4, CLARITY 3, OVER
(THIS IS) TEAM BRAVO, OUT.

---
Example
ALL STATIONS, THIS IS SAR BASE, PINCHER CREEK SAR WILL BE CONDUCTING RADIO TRAINING ON THIS CHANNEL UNTIL 2200 HOURS. OUT

---
Example
ALL SAR TEAMS, THIS IS BASE, RETURN TO BASE. TEAM ALPHA ACKNOWLEDGE OVER
(THIS IS) TEAM ALPHA ROGER (OVER)
TEAM BRAVO, ACKNOWLEDGE (OVER)
(THIS IS) TEAM BRAVO WILCO OVER
TEAM CHARLIE, ACKNOWLEDGE (OVER)
(THIS IS) TEAM CHARLIE WILCO (OVER)
(THIS IS) SAR BASE. OUT.

---
Example
TEAM ALPHA, THIS IS BASE, OVER
BASE, GO AHEAD
TEAM ALPHA PLEASE RELAY FOLLOWING MESSAGE TO TEAM BRAVO PROCEED 1 MILE EAST ON HIGHWAY 507 OVER
THIS IS ALPHA, WILCO, OUT.

---
Example (cont.)
TEAM BRAVO, THIS IS ALPHA OVER
TEAM ALPHA, GO AHEAD
MESSAGE FROM BASE READS: PROCEED 1 MILE EAST ON HIGHWAY 507 OVER
TEAM ALPHA, ROGER. OUT.

---
Logging
ICS-309 form
PCSAR Doc-51

---
Canadian Law
must identify yourself
profane language
false distress
e.g. tests that seem real
privacy

---
Acknowledgments
SAR Alberta Telecommunications Training Standard
  - Rick Koinberg (VE6RAK)
  - Jack Humpries (VA6IX)
  - Bill Heise (VE6SAS)
  - Lyn Michaud (VE6OGN)
Earlier lesson plans
  - Jake Waiboer, Chris Jorgensen

---
Questions?
Brett Wuth <wuth@acm.org> (VA6WUT)
  - Download from pcsar.webhop.org
  - Original content copyright © 2010, Brett Wuth. This work is licensed under the Creative Commons Attribution-ShareAlike 2.0 Canada License. To view a copy of this license, visit http://creativecommons.org/licenses/by-sa/2.0/ca/ or send a letter to Creative Commons, 559 Nathan Abbott Way, Stanford, California 94305, USA.